## Slide 1: Top level view
clk
module add1
real verilog primitive
16 bits adder
module turbosim
(student design)
machine with few rams and
control logic capable of
calculating event propagation
through a logic network
module sim_project
stimuli generation, based on cmd from control logic, it generates 2 16bits number used as adder operands
Add1 sniffer : logic that record each net change inside add1 (ports as well) and generates a readable VCD list. Ready for further comparison
control logic :based on done indication from turbosim, coordinated drive of new change set, launch turbosim and reads the last operation results from tubosim output fifo
DUT Input sniffer Formatter, sense dut input changes and drive them the input fifo of turbosim.
Output Formatter :based on done indication from control logic, and empty from output fifo, reads the last operation results from tubosim output fifo and and convert it to VCD
ready for further comparison

## Slide 2: Scope of project
Support verilog primitive logic network (netlists).
Single module, no hierarchy
No feedback network, only feed-forward. (support is optional)
No support for signal strength.
Supports 4 values 0,1,X, Z
Support single delay construct per instance (#0.433), 433 ps.
Reference DUT (design under test) will be an arbitrary delay adder netlist.

## Slide 3: Scope of project (1)
Up to 32 input bits per DUT
Well behaved netlists :
  No input to output connection (only buf buf1(o,i))
  Output can not be used as internal net ... or or1(o1,a,b); not not1(o2,o1); // forbidden
  No support for multiple driven nets (contention)
  Fully connected, no floating inputs or dandling outputs (of primitives)

## Slide 4: Netlist example
module add1 ( o, a, b );
output [15:0] o; // single signal in a line declaration
input [15:0] a;
input [15:0] b;
wire n1, n2, n3, n4, n5, n6, n7,
n8, n9, n10, n11, n12, n13,
n14, n15, n16, n17, n18, n19,
n20, n21, n22, n23, n24, n25,
n26, n27, n28, n29, n30, n31,
...
not #(1.482) U15 ( n87, n85 );
// verilog primitive, by order only
not #(1.316) U16 ( n73, n71 );
not #(1.956) U17 ( n120, n118 );
nor #(1.449) U18 ( o[2], n50, n51 );
and #(0.225) U19 ( n51, n52, n53 );
nor #(0.646) U20 ( n50, n52, n53 );
nand #(0.592) U21 ( n53, n54, n55 );
nor #(1.762) U22 ( o[3], n43, n44 );
and #(0.331) U23 ( n44, n45, n46 );
nor #(0.068) U24 ( n43, n45, n46 );
nand #(0.466) U25 ( n46, n47, n48 );
nor #(1.628) U26 ( o[4], n36, n37 );

## Slide 5: Test Setup
Mostly provided by me
The real adder module is instantiated.
The student design Turbosim is instantiated.
Testbench stimulate both design.
Real adder internal and external nets change is recorded by the testbench, readable format. (code is in place)
Turbosim results is read from turbosim output fifo
Testbench translate the read data to a readable format, in a way that files can be compared side by side
Add1
real adder
turbosim
clk, rst
No clk to real adder
add1 does not get clk and rst, its a real
combinatorial network that will stabilize
in ~30ns in simulator space.
Turbosim gets clk
as turbosim is a machine loaded with
add1 structure compiled into tutbosim
data-structure. It will take turbosim
many cycles to calculate the final stable
state of the network

## Slide 6: IN/OUT fifo data structure
Inputs fifo
32 entries, 32 bits each
output fifo
8 entries, 32 bits each
Net name to net index dictionary
# // 3 a[12]
# // 4 a[13]
# // 5 a[14]
# // 6 a[15]
# // 7 a[1]
# // 8 a[2]
# // 9 a[3]
# // 10 a[4]
# // 11 a[5]
# // 12 a[6]
# // 13 a[7]
# // 14 a[8]
# // 15 a[9]
# // 16 b[0]
......
# // 122 n32
# // 123 n33
# // 124 n34
# // 125 n35
# // 126 n36
# // 127 n37
# // 128 n38
# // 129 n39
# // 130 n4
# // 131 n40
# // 132 n41
# // 133 n42
# // 134 n43
# // 135 n44
# // 136 n45
testbench
turbosim
Input/output fifo entry |  | 
[31:30] | [29:16] | [15:0]
Net new value | Net index | time

## Slide 7: Input change set
Input fifo used to communicate input net changes to the accelerator.
Up to 32 external changes supported
Changes should be written sorted by time.
All inputs change at the same instant is the Basic usage model that must be supported.
Supporting a gradual net change set is highly appreciated
Supporting internal nets change (force implementation) is .....
1 3 0
0 16 0
1 4 0
1 19 0
.....
up to 32 events
1 3 0
0 16 14
1 4 17
1 19 17
.....
up to 32 events
Gradual change list :
net 3 change at time 0, net 16 change at
time 14, net 4 change at time 17.
all times in pico seconds
net index to net name conversion is
provided.

## Slide 8: Cell data structure
// table may be used turbo sim to hold the cell functionality delay and connectivity
// table width is 88 bits
// where first 4 bits holds the primitive type
// next is 16 bits that holds the primitive delay in ps
// next is 12 bits the holds the net index of the output pin - pin0 bit 11 is set if exist
// next is 12 bits the holds the net index of the input pin - pinX bit 11 is set if exist
// there are 4 such fields
// next is 4 bits for the current output value, set to x, R/W field
// next is 4 bits control that can be used for whatever, also R/W field
0_0327_871_84e_000_000_000_2_0 // 0 U10 | not 807 ps n24 n140 UC UC UC val x, ctl
5_019e_833_811_834_000_000_2_0 // 1 U100 | nand 414 ps n116 b[10] n117 UC UC val x, ctl
5_030c_834_835_836_000_000_2_0 // 2 U101 | nand 780 ps n117 n118 n119 UC UC val x, ctl
2_0510_84e_84f_850_000_000_2_0 // 3 U102 | and 1296 ps n140 n141 n142 UC UC val x, ctl
5_069c_84f_80b_879_000_000_2_0 // 4 U103 | nand 1692 ps n141 a[5] n31 UC UC val x, ctl
5_0511_850_81b_851_000_000_2_0 // 5 U104 | nand 1297 ps n142 b[5] n143 UC UC val x, ctl
5_04d1_851_852_87d_000_000_2_0 // 6 U105 | nand 1233 ps n143 n144 n35 UC UC val x, ctl
2_0314_8c0_826_827_000_000_2_0 // 7 U106 | and 788 ps n96 n104 n105 UC UC val x, ctl
5_00bb_826_802_82b_000_000_2_0 // 8 U107 | nand 187 ps n104 a[11] n109 UC UC val x, ctl
5_015a_827_812_828_000_000_2_0 // 9 U108 | nand 346 ps n105 b[11] n106 UC UC val x, ctl
5_00a2_828_829_82a_000_000_2_0 // 10 U109 | nand 162 ps n106 n107 n108 UC UC val x, ctl
0_00b3_869_849_000_000_000_2_0 // 11 U11 | not 179 ps n17 n136 UC UC UC val x, ctl
2_02eb_849_84a_84b_000_000_2_0 // 12 U110 | and 747 ps n136 n137 n138 UC UC val x, ctl
....

## Slide 9: net data structure
// table may be used turbosim to hold the net connectivity
// table width is 84bits, 5x16+4
// where 5 = 1 driver + 4 loads
// where 16 = 12 + 4, 12 = cell index + bit 11 set if exist
// where 4 = pin index of driving/load cell
// where the last 4 bits reflects the number of loads on net
000_0_84a_1_848_1_000_0_000_0_2 // 0 a[0] | no dpin ,U167 pin1 ,U165 pin1 ,no load ,no load ,n loads 2
000_0_83f_1_8b3_1_000_0_000_0_2 // 1 a[10] | no dpin ,U157 pin1 ,U99 pin1 ,no load ,no load ,n loads 2
000_0_808_1_840_1_000_0_000_0_2 // 2 a[11] | no dpin ,U107 pin1 ,U158 pin1 ,no load ,no load ,n loads 2
000_0_811_1_841_1_000_0_000_0_2 // 3 a[12] | no dpin ,U115 pin1 ,U159 pin1 ,no load ,no load ,n loads 2
000_0_843_1_81a_1_000_0_000_0_2 // 4 a[13] | no dpin ,U160 pin1 ,U123 pin1 ,no load ,no load ,n loads 2
000_0_836_1_844_1_000_0_000_0_2 // 5 a[14] | no dpin ,U149 pin1 ,U161 pin1 ,no load ,no load ,n loads 2
000_0_825_1_000_0_000_0_000_0_1 // 6 a[15] | no dpin ,U133 pin1 ,no load ,no load ,no load ,n loads 1
000_0_846_1_8a3_1_000_0_000_0_2 // 7 a[1] | no dpin ,U163 pin1 ,U84 pin1 ,no load ,no load ,n loads 2
000_0_8a6_1_838_1_000_0_000_0_2 // 8 a[2] | no dpin ,U87 pin1 ,U150 pin1 ,no load ,no load ,n loads 2
....
000_0_845_1_81e_1_855_2_000_0_3 // 31 b[9] | no dpin ,U162 pin1 ,U127 pin1 ,U177 pin2 ,no load ,n loads 3
87b_0_879_1_000_0_000_0_000_0_1 // 32 n1 | U48 pin0 ,U46 pin1 ,no load ,no load ,no load ,n loads 1
816_0_877_1_89d_2_876_1_000_0_3 // 33 n10 | U12 pin0 ,U44 pin1 ,U79 pin2 ,U43 pin1 ,no load ,n loads 3
887_0_886_2_000_0_000_0_000_0_1 // 34 n100 | U59 pin0 ,U58 pin2 ,no load ,no load ,no load ,n loads 1
88a_0_887_2_889_2_000_0_000_0_2 // 35 n101 | U61 pin0 ,U59 pin2 ,U60 pin2 ,no load ,no load ,n loads 2
859_0_88a_1_000_0_000_0_000_0_1 // 36 n102 | U180 pin0 ,U61 pin1 ,no load ,no load ,no load ,n loads 1
830_0_88a_2_000_0_000_0_000_0_1 // 38 n104 | U107 pin0 ,U106 pin1 ,no load ,no load ,no load ,n loads 1
.....

## Slide 10: Update event
“Every change in value of a net or variable in the circuit being simulated, as well as the named event, is considered an update event”.

## Slide 11: Evaluation event
“Processes are sensitive to update events. When an update event is executed, all the processes that are sensitive to that event are evaluated in an arbitrary order. The evaluation of a process is also an event, known as an evaluation event”

## Slide 12: The stratified event queue
Events can be added to any queue
Events removed only from active region.
Future events
Monitor events
Active events
In-Active events
Nonblocking assign update events

## Slide 13: Events flow
while (there are events) {
if (no active events) {
if (there are inactive events) {
activate all inactive events;
}
else if (there are nonblocking assign update events) { // zero delay support ?
activate all nonblocking assign update events;
}
else if (there are monitor events) { // no support
activate all monitor events;
}
else {
advance T to the next event time;
activate all inactive events for time T;
}
}
E = any active event;
if (E is an update event) {
update the modified object;
add evaluation events for sensitive processes to event
queue;
} else { /* shall be an evaluation event */
evaluate the process;
add update events to the event queue;
}
}

## Slide 14: Example (1)
Assuming TB changed simultaneously the ports a and b. then =>
  We will add two updates events to the active queue.

## Slide 15: Example (2)
Since no other events in the event queue. then =>
  We can remove the two events even simultaneously (if we can) from the bottom of event queue

## Slide 16: Example (3)
We consider each event, if its an update event (it is!) then =>
  We consult the nets database and insert an evaluation event to What Q ? (need to come with strategy).
  In case of “a”, we add 2 evaluation events, for U1 and U2.
  For “b” we add evaluation event for U5

## Slide 17: Example (4)
In the background, the event Q is working to restore the “sorted state” note that we need our sort to be what is called “stable”

## Slide 18: Example (5)
If event Q is ready, ie. “sorted” then =>
  We fetch one of the events (from the active Q), in our case it should be an evaluation event.
  We evaluate the process (the gate) with the most recently known input pins values.
  If the evaluation results in a change of the gate output, then we insert an update event to what Q ? (have to come with a solid strategy….)

## Slide 19: Event Queue data structure
General structure of event Q
Field width to be specified by student
Filed encoding to be specified by student
Design should maintain an empty container that holds the addresses of empty records.
During init phase, this container should be field by ascending addresses
Q size => 512 entries. ???
Empty container should be fifo based
Event Q should be dual or single port RAM
Event queue entry |  |  |  |  | 
Event type | New value | Object index | time | Prev event ? | Next event ?

## Slide 20: utilities
parse_verilog_netlist.pl <verilog module file>
First level support – simple verilog, no special package support.
Reads the verilog file and generates several files/tables/perl data structures, that are used by testbench and design.
Also generates <module_name>.pl, perl representation of all data in module. This can be used by the student for further processing.
maxn@maxn-desktop:~/verilog_try$ lth
total 1000
-rw-r--r-- 1 maxn maxn 215245 2010-03-14 12:33 add1.pl
-rw-r--r-- 1 maxn maxn 22163 2010-03-14 12:33 cell_index_to_data_mem.v
-rw-r--r-- 1 maxn maxn 25942 2010-03-14 12:33 net_index_to_data_mem.v
-rw-r--r-- 1 maxn maxn 21360 2010-03-14 12:33 net_index_to_name_mem.v
-rw-r--r-- 1 maxn maxn 6502 2010-03-14 12:33 ref_dut_input_sniffer.v
-rw-r--r-- 1 maxn maxn 33334 2010-03-14 12:33 ref_dut_sniffer.v
-

## Slide 21: Readable VCD format
VCD – Value Change Dump